## Slide 1: Assembly Language for x86 Processors
Copyright © 2020, 2015, 2011 Pearson Education, Inc. All Rights Reserved
x86 Processor Architecture
Chapter 2
Eighth Edition

## Slide 2: Chapter Overview
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 3: General Concepts
Basic microcomputer design
Instruction execution cycle
Reading from memory
How programs run

## Slide 4: Basic Microcomputer Design
clock synchronizes CPU operations
control unit (CU) coordinates sequence of execution steps
ALU performs arithmetic and bitwise processing

## Slide 5: Clock
synchronizes all CPU and BUS operations
machine (clock) cycle measures time of a single operation
clock is used to trigger events

## Slide 6: What's Next (1 of 5)
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-Bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 7: Instruction Execution Cycle
Fetch
Decode
Fetch operands
Execute
Store output

## Slide 8: Reading from Memory
Multiple machine cycles are required when reading from memory, because it responds much more slowly than the CPU. The steps are:
  Place the address of the value you want to read on the address bus.
  Assert (changing the value of) the processor’s RD (read) pin.
  Wait one clock cycle for the memory chips to respond.
  Copy the data from the data bus into the destination operand

## Slide 9: Cache Memory
High-speed expensive static RAM both inside and outside the CPU.
  Level-1 cache: inside the CPU
  Level-2 cache: outside the CPU
Cache hit: when data to be read is already in cache memory
Cache miss: when data to be read is not in cache memory.

## Slide 10: How a Program Runs

## Slide 11: IA-32 Processor Architecture
Modes of operation
Basic execution environment
Floating-point unit
Intel Microprocessor history

## Slide 12: Modes of Operation
Virtual-8086 mode
  hybrid of Protected
  each program has its own 8086 computer
Protected mode
  native mode (Windows, Linux)
Real-address mode
  native MS-DOS
System management mode
  power management, system security, diagnostics

## Slide 13: Basic Execution Environment
Addressable memory
General-purpose registers
Index and base registers
Specialized register uses
Status flags
Floating-point, MMX, XMM registers

## Slide 14: Addressable Memory
Protected mode
  4 GB
  32-bit address
Real-address and Virtual-8086 modes
  1 MB space
  20-bit address

## Slide 15: General-Purpose Registers
Named storage locations inside the CPU, optimized for speed.

## Slide 16: Accessing Parts of Registers
Use 8-bit name,16-bit name, or 32-bit name
Applies to EAX, EBX, ECX, and EDX

## Slide 17: Index and Base Registers
Some registers have only a 16-bit name for their lower half:

## Slide 18: Some Specialized Register Uses (1 of 2)
General-Purpose
  EAX – accumulator
  ECX – loop counter
  ESP – stack pointer
  ESI, EDI – index registers
  EBP – extended frame pointer (stack)
Segment
  CS – code segment
  DS – data segment
  SS – stack segment
  ES, FS, GS - additional segments

## Slide 19: Some Specialized Register Uses (2 of 2)
EIP – instruction pointer
EFLAGS
  status and control flags
  each flag is a single binary bit

## Slide 20: Status Flags
Carry
  unsigned arithmetic out of range
Overflow
  signed arithmetic out of range
Sign
  result is negative
Zero
  result is zero
Auxiliary Carry
  carry from bit 3 to bit 4
Parity
  sum of 1 bits is an even number

## Slide 21: Floating-Point, MMX, XMM Registers
Eight 80-bit floating-point data registers
  ST(0), ST(1), . . . , ST(7)
  arranged in a stack
  used for all floating-point arithmetic
Eight 64-bit MMX registers
Eight 128-bit XMM registers for single-instruction multiple-data (SIMD) operations

## Slide 22: What's Next (2 of 5)
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-Bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 23: IA-32 Memory Management
Real-address mode
Calculating linear addresses
Protected mode
Multi-segment model
Paging

## Slide 24: Protected Mode
4 GB addressable RAM
  (00000000 to FFFFFFFFh)
Each program assigned a memory partition which is protected from other programs
Designed for multitasking
Supported by Linux & MS-Windows

## Slide 25: What's Next (3 of 5)
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-Bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 26: 64-Bit Processors
64-Bit Operation Modes
  Compatibility mode – can run existing 16-bit and 32-bit applications (Windows supports only 32-bit apps in this mode)
  64-bit mode – Windows 64 uses this
Basic Execution Environment
  addresses can be 64 bits (48 bits, in practice)
  16 64-bit general purpose registers
  64-bit instruction pointer named RIP

## Slide 27: 64-Bit General Purpose Registers
32-bit general purpose registers:
  EAX, EBX, ECX, EDX, EDI, ESI, EBP, ESP, R8D, R9D, R10D, R11D, R12D, R13D, R14D, R15D
64-bit general purpose registers:
  RAX, RBX, RCX, RDX, RDI, RSI, RBP, RSP, R8, R9, R10, R11, R12, R13, R14, R15

## Slide 28: What's Next (4 of 5)
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-Bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 29: Components of an IA-32 Microcomputer
Motherboard
Video output
Memory
Input-output ports

## Slide 30: Motherboard
CPU socket
External cache memory slots
Main memory slots
BIOS chips
Sound synthesizer chip (optional)
Video controller chip (optional)
IDE, parallel, serial, USB, video, keyboard, joystick, network, and mouse connectors
PCI bus connectors (expansion cards)

## Slide 31: Intel D850MD Motherboard
Source: Intel® Desktop Board D850MD/D850MV Technical Product Specification
dynamic RAM
Pentium 4 socket
Speaker
IDE drive connectors
AGP slot
Battery
Video
Power connector
Diskette connector
PCI slots
Firmware hub
Audio chip
mouse, keyboard, parallel, serial, and USB connectors
memory controller hub

## Slide 32: Intel 965 Express Chipset

## Slide 33: Video Output
* This link may change over time.
Video controller
  on motherboard, or on expansion card
  AGP (accelerated graphics port technology)*
Video memory (VRAM)
Video CRT Display
  uses raster scanning
  horizontal retrace
  vertical retrace
Direct digital LCD monitors
  no raster scanning required

## Slide 34: Sample Video Controller (ATI Corp.) (1 of 2)
128-bit 3D graphics performance powered by RAGE™ 128 PRO
3D graphics performance
Intelligent TV-Tuner with Digital VCR
TV-ON-DEMAND™
Interactive Program Guide
Still image and MPEG-2 motion video capture
Video editing
Hardware DVD video playback
Video output to TV or VCR

## Slide 35: Sample Video Controller (ATI Corp.) (2 of 2)

## Slide 36: Memory (1 of 2)
ROM
  read-only memory
EPROM
  erasable programmable read-only memory
Dynamic RAM (DRAM)
  inexpensive; must be refreshed constantly
Static RAM (SRAM)
  expensive; used for cache memory; no refresh required

## Slide 37: Memory (2 of 2)
Video RAM (VRAM)
  dual ported; optimized for constant video refresh
CMOS RAM
  complimentary metal-oxide semiconductor
  system setup information
See: Intel platform memory (Intel technology brief: link address may change)

## Slide 38: Input-Output Ports
USB (universal serial bus)
  intelligent high-speed connection to devices
  up to 12 megabits/second
  USB hub connects multiple devices
  enumeration: computer queries devices
  supports hot connections
Parallel
  short cable, high speed
  common for printers
  bidirectional, parallel data transfer
  Intel 8255 controller chip

## Slide 39: Input-Output Ports (cont)
Serial
  RS-232 serial port
  one bit at a time
  uses long cables and modems
  16550 UART (universal asynchronous receiver transmitter)
  programmable in assembly language

## Slide 40: Device Interfaces
ATA host adapters
  intelligent drive electronics (hard drive, CDROM)
SATA (Serial ATA)
  inexpensive, fast, bidirectional
FireWire
  high speed (800 MB/sec), many devices at once
Bluetooth
  small amounts of data, short distances, low power usage
Wi-Fi (wireless Ethernet)
  IEEE 802.11 standard, faster than Bluetooth

## Slide 41: What's Next (5 of 5)
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 42: Levels of Input-Output
Level 3: High-level language function
  examples: C++, Java
  portable, convenient, not always the fastest
Level 2: Operating system
  Application Programming Interface (API)
  extended capabilities, lots of details to master
Level 1: BIOS
  drivers that communicate directly with devices
  OS security may prevent application-level code from working at this level

## Slide 43: Displaying a String of Characters
When a HLL program displays a string of characters, the following steps take place:

## Slide 44: Programming levels
Assembly language programs can perform input-output at each of the following levels:

## Slide 45: Summary
Central Processing Unit (CPU)
Arithmetic Logic Unit (ALU)
Instruction execution cycle
Multitasking
Floating Point Unit (FPU)
Complex Instruction Set
Real mode and Protected mode
Motherboard components
Memory types
Input/Output and access levels

## Slide 46: 42 69 6E 61 72 79
What does this say?

## Slide 47: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.
Notes: If this slide was not included in the original PPT, it should be added.