## Slide 1: Assembly Language for x86 Processors
Copyright © 2020, 2015, 2011 Pearson Education, Inc. All Rights Reserved
Data Transfers, Addressing, and Arithmetic
Chapter 4
Eighth Edition

## Slide 2: Chapter Overview
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions
64-Bit Programming

## Slide 3: Data Transfer Instructions
Operand Types
Instruction Operand Notation
Direct Memory Operands
MOV Instruction
Zero & Sign Extension
XCHG Instruction
Direct-Offset Instructions

## Slide 4: Operand Types
Immediate – a constant integer (8, 16, or 32 bits)
  value is encoded within the instruction
Register – the name of a register
  register name is converted to a number and encoded within the instruction
Memory – reference to a location in memory
  memory address is encoded within the instruction, or a register holds the address of a memory location

## Slide 5: Instruction Operand Notation

## Slide 6: Direct Memory Operands
alternate format
.data
var1 BYTE 10h
.code
mov al,var1 ; AL = 10h
mov al,[var1] ; AL = 10h
A direct memory operand is a named reference to storage in memory
The named reference (label) is automatically dereferenced by the assembler

## Slide 7: MOV Instruction
.data
count BYTE 100
wVal WORD 2
.code
mov bl,count
mov ax,wVal
mov count,al
mov al,wVal ; error
mov ax,count ; error
mov eax,count ; error
Move from source to destination. Syntax:
MOV destination,source
No more than one memory operand permitted
CS, EIP, and IP cannot be the destination
No immediate to segment moves

## Slide 8: Your turn . . . (1 of 12)
.data
bVal BYTE 100
bVal2 BYTE ?
wVal WORD 2
dVal DWORD 5
.code
mov ds,45 immediate move to DS not permitted
mov esi,wVal size mismatch
mov eip,dVal EIP cannot be the destination
mov 25,bVal immediate value cannot be destination
mo bVal2,bVal memory-to-memory move not permitted
Explain why each of the following MOV statements are invalid:

## Slide 9: Zero Extension
The destination must be a register.
mov bl,10001111b
movzx ax,bl ; zero-extension
When you copy a smaller value into a larger destination, the MOVZX instruction fills (extends) the upper half of the destination with zeros.

## Slide 10: Sign Extension
The destination must be a register.
mov bl,10001111b
movsx ax,bl ; sign extension
The MOVSX instruction fills the upper half of the destination with a copy of the source operand's sign bit.

## Slide 11: XCHG Instruction
.data
var1 WORD 1000h
var2 WORD 2000h
.code
xchg ax,bx ; exchange 16-bit regs
xchg ah,al ; exchange 8-bit regs
xchg var1,bx ; exchange mem, reg
xchg eax,ebx ; exchange 32-bit regs
xchg var1,var2 ; error: two memory operands
XCHG exchanges the values of two operands. At least one operand must be a register. No immediate operands are permitted.

## Slide 12: Direct-Offset Operands
Q: Why doesn't arrayB+1 produce 11h?
.data
arrayB BYTE 10h,20h,30h,40h
.code
mov al,arrayB+1 ; AL = 20h
mov al,[arrayB+1] ; alternative notation
A constant offset is added to a data label to produce an effective address (EA). The address is dereferenced to get the value inside its memory location.

## Slide 13: Direct-Offset Operands (cont) (1 of 2)
A constant offset is added to a data label to produce an effective address (EA). The address is dereferenced to get the value inside its memory location.

## Slide 14: Direct-Offset Operands (cont) (2 of 2)
What will happen when they run?
; Will the following statements assemble?
mov ax,[arrayW-2] ; ??
mov eax,[arrayD+16] ; ??
.data
arrayW WORD 1000h,2000h,3000h
arrayD DWORD 1,2,3,4
.code
mov ax,[arrayW+2] ; AX = 2000h
mov ax,[arrayW+4] ; AX = 3000h
mov eax,[arrayD+4] ; EAX = 00000002h

## Slide 15: Your turn. . . (2 of 12)
mov eax,arrayD
xchg eax,[arrayD+4]
Write a program that rearranges the values of three doubleword values in the following array as: 3, 1, 2.
.data
arrayD DWORD 1,2,3
Step1: copy the first value into EAX and exchange it with the value in the second position

## Slide 16: Your turn. . . (3 of 12)
xchg eax,[arrayD+8]
mov arrayD,eax
Step 2: Exchange EAX with the third array value and copy the value in EAX to the first array position.

## Slide 17: Evaluate this . . .
.data
myBytes BYTE 80h,66h,0A5h
Any other possibilities?
mov al,myBytes
add al,[myBytes+1]
add al,[myBytes+2]
What is your evaluation of the following code?
.data
myBytes BYTE 80h,66h,0A5h
We want to write a program that adds the following three bytes:

## Slide 18: Evaluate this . . . (cont)
Yes: Move zero to BX before the MOVZX instruction.
movzx ax,myBytes
mov bl,[myBytes+1]
add ax,bx
mov bl,[myBytes+2]
add ax,bx ; AX = sum
How about the following code. Is anything missing?

## Slide 19: What's Next (1 of 5)
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions
64-Bit Programming

## Slide 20: Addition and Subtraction
INC and DEC Instructions
ADD and SUB Instructions
NEG Instruction
Implementing Arithmetic Expressions
Flags Affected by Arithmetic
  Zero
  Sign
  Carry
  Overflow

## Slide 21: INC and DEC Instructions
Add 1, subtract 1 from destination operand
  operand may be register or memory
INC destination
  Logic: destination  destination + 1
DEC destination
  Logic: destination  destination – 1

## Slide 22: INC and DEC Examples
.data
myWord WORD 1000h
myDword DWORD 10000000h
.code
inc myWord ; 1001h
dec myWord ; 1000h
inc myDword ; 10000001h
mov ax,00FFh
inc ax ; AX = 0100h
mov ax,00FFh
inc al ; AX = 0000h

## Slide 23: Your turn... (4 of 12)
.data
myByte BYTE 0FFh, 0
.code
mov al,myByte ; AL = FFh
mov ah,[myByte+1] ; AH = 00h
dec ah ; AH = FFh
inc al ; AL = 00h
dec ax ; AX = FEFF
Show the value of the destination operand after each of the following instructions executes:

## Slide 24: ADD and SUB Instructions
ADD destination, source
  Logic: destination  destination + source
SUB destination, source
  Logic: destination  destination – source
Same operand rules as for the MOV instruction

## Slide 25: ADD and SUB Examples
.data
var1 DWORD 10000h
var2 DWORD 20000h
.code ; ---EAX---
mov eax,var1 ; 00010000h
add eax,var2 ; 00030000h
add ax,0FFFFh ; 0003FFFFh
add eax,1 ; 00040000h
sub ax,1 ; 0004FFFFh

## Slide 26: NEG (negate) Instruction
Suppose AX contains –32,768 and we apply NEG to it. Will the result be valid?
.data
valB BYTE -1
valW WORD +32767
.code
mov al,valB ; AL = -1
neg al ; AL = +1
neg valW ; valW = -32767
Reverses the sign of an operand. Operand can be a register or memory operand.

## Slide 27: NEG Instruction and the Flags
.data
valB BYTE 1,0
valC SBYTE -128
.code
neg valB ; CF = 1, OF = 0
neg [valB + 1] ; CF = 0, OF = 0
neg valC ; CF = 1, OF = 1
The processor implements NEG using the following internal operation:
SUB 0,operand
Any nonzero operand causes the Carry flag to be set.

## Slide 28: Implementing Arithmetic Expressions (1 of 2)
HLL compilers translate mathematical expressions into assembly language. You can do it also. For example:
Rval = -Xval + (Yval – Zval)

## Slide 29: Implementing Arithmetic Expressions (2 of 2)
Rval DWORD ?
Xval DWORD 26
Yval DWORD 30
Zval DWORD 40
.code
mov eax,Xval
neg eax ; EAX = -26
mov ebx,Yval
sub ebx,Zval ; EBX = -10
add eax,ebx
mov Rval,eax ; -36

## Slide 30: Your turn... (5 of 12)
mov ebx,Yval
neg ebx
add ebx,Zval
mov eax,Xval
sub eax,ebx
mov Rval,eax
Translate the following expression into assembly language. Do not permit Xval, Yval, or Zval to be modified:
Rval = Xval - (-Yval + Zval)
Assume that all values are signed doublewords.

## Slide 31: Flags Affected by Arithmetic
The ALU has a number of status flags that reflect the outcome of arithmetic (and bitwise) operations
  based on the contents of the destination operand
Essential flags:
  Zero flag – set when destination equals zero
  Sign flag – set when destination is negative
  Carry flag – set when unsigned value is out of range
  Overflow flag – set when signed value is out of range
The MOV instruction never affects the flags.

## Slide 32: Concept Map
You can use diagrams such as these to express the relationships between assembly language concepts.
status flags
branching logic
arithmetic & bitwise operations
part of
used by
provide
attached to
affect
executes
conditional jumps
executes
CPU
ALU

## Slide 33: Zero Flag (ZF)
Remember...
A flag is set when it equals 1.
A flag is clear when it equals 0.
mov cx,1
sub cx,1 ; CX = 0, ZF = 1
mov ax,0FFFFh
inc ax ; AX = 0, ZF = 1
inc ax ; AX = 1, ZF = 0
The Zero flag is set when the result of an operation produces zero in the destination operand.

## Slide 34: Sign Flag (SF)
mov al,0
sub al,1 ; AL = 11111111b, SF = 1
add al,2 ; AL = 00000001b, SF = 0
The sign flag is a copy of the destination's highest bit:
mov cx,0
sub cx,1 ; CX = -1, SF = 1
add cx,2 ; CX = 1, SF = 0
The Sign flag is set when the destination operand is negative. The flag is clear when the destination is positive.

## Slide 35: Signed and Unsigned Integers A Hardware Viewpoint
All CPU instructions operate exactly the same on signed and unsigned integers
The CPU cannot distinguish between signed and unsigned integers
YOU, the programmer, are solely responsible for using the correct data type with each instruction

## Slide 36: Overflow and Carry Flags A Hardware Viewpoint
MSB = Most Significant Bit (high-order bit)
XOR = eXclusive-OR operation
NEG = Negate (same as SUB 0,operand )
How the ADD instruction affects OF and CF:
  CF = (carry out of the MSB)
  OF = CF XOR MSB
How the SUB instruction affects OF and CF:
  CF = INVERT (carry out of the MSB)
  negate the source and add it to the destination
  OF = CF XOR MSB

## Slide 37: Carry Flag (CF)
mov al,0FFh
add al,1 ; CF = 1, AL = 00
; Try to go below zero:
mov al,0
sub al,1 ; CF = 1, AL = FF
The Carry flag is set when the result of an operation generates an unsigned value that is out of range (too big or too small for the destination operand).

## Slide 38: Your turn . . . (6 of 12)
mov ax,00FFh
add ax,1 ; AX= 0100h SF = 0 ZF= 0 CF= 0
sub ax,1 ; AX= 00FFh SF = 0 ZF= 0 CF= 0
add al,1 ; AL= 00h SF = 0 ZF= 1 CF= 1
mov bh,6Ch
add bh,95h ; BH= 01h SF = 0 ZF= 0 CF= 1
mov al,2
sub al,3 ; AL= FFh SF = 1 ZF= 0 CF= 1
For each of the following marked entries, show the values of the destination operand and the Sign, Zero, and Carry flags:

## Slide 39: Overflow Flag (OF)
The two examples are identical at the binary level because 7Fh equals +127. To determine the value of the destination operand, it is often easier to calculate in hexadecimal.
; Example 1
mov al,+127
add al,1 ; OF = 1, AL = ??
; Example 2
mov al,7Fh ; OF = 1, AL = 80h
add al,1
The Overflow flag is set when the signed result of an operation is invalid or out of range.

## Slide 40: A Rule of Thumb
What will be the values of the Overflow flag?
mov al,80h
add al,92h ; OF = 1
mov al,-2
add al,+127 ; OF = 0
When adding two integers, remember that the Overflow flag is only set when . . .
  Two positive operands are added and their sum is negative
  Two negative operands are added and their sum is positive

## Slide 41: Your turn . . . (7 of 12)
mov al,-128
neg al ; CF = 1 OF = 1
mov ax,8000h
add ax,2 ; CF = 0 OF = 0
mov ax,0
sub ax,2 ; CF = 1 OF = 0
mov al,-5
sub al,+125 ; OF = 1
What will be the values of the given flags after each operation?

## Slide 42: What's Next (2 of 5)
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions
64-Bit Programming

## Slide 43: Data-Related Operators and Directives
OFFSET Operator
PTR Operator
TYPE Operator
LENGTHOF Operator
SIZEOF Operator
LABEL Directive

## Slide 44: OFFSET Operator
The Protected-mode programs we write use only a single segment (flat memory model).
OFFSET returns the distance in bytes, of a label from the beginning of its enclosing segment
  Protected mode: 32 bits
  Real mode: 16 bits

## Slide 45: OFFSET Examples
.data
bVal BYTE ?
wVal WORD ?
dVal DWORD ?
dVal2 DWORD ?
.code
mov esi,OFFSET bVal ; ESI = 00404000
mov esi,OFFSET wVal ; ESI = 00404001
mov esi,OFFSET dVal ; ESI = 00404003
mov esi,OFFSET dVal2 ; ESI = 00404007
Let's assume that the data segment begins at 00404000h:

## Slide 46: Relating to C/C++
; Assembly language:
.data
array BYTE 1000 DUP(?)
.code
mov esi,OFFSET array
// C++ version:
char array[1000];
char * p = array;
The value returned by OFFSET is a pointer. Compare the following code written for both C++ and assembly language:

## Slide 47: PTR Operator
Little endian order is used when storing data in memory (see Section 3.4.9).
.data
myDouble DWORD 12345678h
.code
mov ax,myDouble ; error – why?
mov ax,WORD PTR myDouble ; loads 5678h
mov WORD PTR myDouble,4321h ; saves 4321h
Overrides the default type of a label (variable). Provides the flexibility to access part of a variable.

## Slide 48: Little Endian Order
When integers are loaded from memory into registers, the bytes are automatically re-reversed into their correct positions.
Little endian order refers to the way Intel stores integers in memory.
Multi-byte integers are stored in reverse order, with the least significant byte stored at the lowest address
For example, the doubleword 12345678h would be stored as:

## Slide 49: PTR Operator Examples
mov al,BYTE PTR myDouble ; AL = 78h
mov al,BYTE PTR [myDouble+1] ; AL = 56h
mov al,BYTE PTR [myDouble+2] ; AL = 34h
mov ax,WORD PTR myDouble ; AX = 5678h
mov ax,WORD PTR [myDouble+2] ; AX = 1234h
.data
myDouble DWORD 12345678h

## Slide 50: PTR Operator (cont)
.data
myBytes BYTE 12h,34h,56h,78h
.code
mov ax,WORD PTR [myBytes] ; AX = 3412h
mov ax,WORD PTR [myBytes+2] ; AX = 7856h
mov eax,DWORD PTR myBytes ; EAX = 78563412h
PTR can also be used to combine elements of a smaller data type and move them into a larger operand. The CPU will automatically reverse the bytes.

## Slide 51: Your turn . . . (8 of 12)
.data
varB BYTE 65h,31h,02h,05h
varW WORD 6543h,1202h
varD DWORD 12345678h
.code
mov ax,WORD PTR [varB+2] ; a. 0502h
mov bl,BYTE PTR varD ; b. 78h
mov bl,BYTE PTR [varW+2] ; c. 02h
mov ax,WORD PTR [varD+2] ; d. 1234h
mov eax,DWORD PTR varW ; e. 12026543h
Write down the value of each destination operand:

## Slide 52: TYPE Operator
.data
var1 BYTE ?
var2 WORD ?
var3 DWORD ?
var4 QWORD ?
.code
mov eax,TYPE var1 ; 1
mov eax,TYPE var2 ; 2
mov eax,TYPE var3 ; 4
mov eax,TYPE var4 ; 8
The TYPE operator returns the size, in bytes, of a single element of a data declaration.

## Slide 53: LENGTHOF Operator
.data LENGTHOF
byte1 BYTE 10,20,30 ; 3
array1 WORD 30 DUP(?),0,0 ; 32
array2 WORD 5 DUP(3 DUP(?)) ; 15
array3 DWORD 1,2,3,4 ; 4
digitStr BYTE "12345678",0 ; 9
.code
mov ecx,LENGTHOF array1 ; 32
The LENGTHOF operator counts the number of elements in a single data declaration.

## Slide 54: SIZEOF Operator
.data SIZEOF
byte1 BYTE 10,20,30 ; 3
array1 WORD 30 DUP(?),0,0 ; 64
array2 WORD 5 DUP(3 DUP(?)) ; 30
array3 DWORD 1,2,3,4 ; 16
digitStr BYTE "12345678",0 ; 9
.code
mov ecx,SIZEOF array1 ; 64
The SIZEOF operator returns a value that is equivalent to multiplying LENGTHOF by TYPE.

## Slide 55: Spanning Multiple Lines (1 of 2)
.data
array WORD 10,20,
30,40,
50,60
.code
mov eax,LENGTHOF array ; 6
mov ebx,SIZEOF array ; 12
A data declaration spans multiple lines if each line (except the last) ends with a comma. The LENGTHOF and SIZEOF operators include all lines belonging to the declaration:

## Slide 56: Spanning Multiple Lines (2 of 2)
.data
array WORD 10,20
WORD 30,40
WORD 50,60
.code
mov eax,LENGTHOF array ; 2
mov ebx,SIZEOF array ; 4
In the following example, array identifies only the first WORD declaration. Compare the values returned by LENGTHOF and SIZEOF here to those in the previous slide:

## Slide 57: LABEL Directive
.data
dwList LABEL DWORD
wordList LABEL WORD
intList BYTE 00h,10h,00h,20h
.code
mov eax,dwList ; 20001000h
mov cx,wordList ; 1000h
mov dl,intList ; 00h
Assigns an alternate label name and type to an existing storage location
LABEL does not allocate any storage of its own
Removes the need for the PTR operator

## Slide 58: What's Next (3 of 5)
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions
64-Bit Programming

## Slide 59: Indirect Addressing
Indirect Operands
Array Sum Example
Indexed Operands
Pointers

## Slide 60: Indirect Operands (1 of 2)
.data
val1 BYTE 10h,20h,30h
.code
mov esi,OFFSET val1
mov al,[esi] ; dereference ESI (AL = 10h)
inc esi
mov al,[esi] ; AL = 20h
inc esi
mov al,[esi] ; AL = 30h
An indirect operand holds the address of a variable, usually an array or string. It can be dereferenced (just like a pointer).

## Slide 61: Indirect Operands (2 of 2)
yes, because [esi] could point to a byte, word, or doubleword
Should PTR be used here?
add [esi],20
.data
myCount WORD 0
.code
mov esi,OFFSET myCount
inc [esi] ; error: ambiguous
inc WORD PTR [esi] ; ok
Use PTR to clarify the size attribute of a memory operand.

## Slide 62: Array Sum Example
ToDo: Modify this example for an array of doublewords.
.data
arrayW WORD 1000h,2000h,3000h
.code
  mov esi,OFFSET arrayW
  mov ax,[esi]
  add esi,2 ; or: add esi,TYPE arrayW
  add ax,[esi]
  add esi,2
  add ax,[esi] ; AX = sum of the array
Indirect operands are ideal for traversing an array. Note that the register in brackets must be incremented by a value that matches the array type.

## Slide 63: Indexed Operands
ToDo: Modify this example for an array of doublewords.
.data
arrayW WORD 1000h,2000h,3000h
.code
mov esi,0
mov ax,[arrayW + esi] ; AX = 1000h
mov ax,arrayW[esi] ; alternate format
add esi,2
add ax,[arrayW + esi]
etc.
An indexed operand adds a constant to a register to generate an effective address. There are two notational forms:
[label + reg] label[reg]

## Slide 64: Index Scaling
.data
arrayB BYTE 0,1,2,3,4,5
arrayW WORD 0,1,2,3,4,5
arrayD DWORD 0,1,2,3,4,5
.code
mov esi,4
mov al,arrayB[esi*TYPE arrayB] ; 04
mov bx,arrayW[esi*TYPE arrayW] ; 0004
mov edx,arrayD[esi*TYPE arrayD] ; 00000004
You can scale an indirect or indexed operand to the offset of an array element. This is done by multiplying the index by the array's TYPE:

## Slide 65: Pointers
Alternate format:
ptrW DWORD OFFSET arrayW
.data
arrayW WORD 1000h,2000h,3000h
ptrW DWORD arrayW
.code
mov esi,ptrW
mov ax,[esi] ; AX = 1000h
You can declare a pointer variable that contains the offset of another variable.

## Slide 66: What's Next (4 of 5)
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions
64-Bit Programming

## Slide 67: JMP and LOOP Instructions
JMP Instruction
LOOP Instruction
LOOP Example
Summing an Integer Array
Copying a String

## Slide 68: JMP Instruction
A jump outside the current procedure must be to a special type of label called a global label (see Section 5.5.2.3 for details).
top:
.
.
jmp top
JMP is an unconditional jump to a label that is usually within the same procedure.
Syntax: JMP target
Logic: EIP  target
Example:

## Slide 69: LOOP Instruction
The LOOP instruction creates a counting loop
Syntax: LOOP target
Logic:
  ECX  ECX – 1
  if ECX != 0, jump to target
Implementation:
  The assembler calculates the distance, in bytes, between the offset of the following instruction and the offset of the target label. It is called the relative offset.
  The relative offset is added to EIP.

## Slide 70: LOOP Example
When LOOP is assembled, the current location = 0000000E (offset of the next instruction). –5 (FBh) is added to the the current location, causing a jump to location 00000009:
00000009  0000000E + FB
00000000 66 B8 0000 mov ax,0
00000004 B9 00000005 mov ecx,5
00000009 66 03 C1 L1: add ax,cx
0000000C E2 FB loop L1
0000000E
Offset machine code source code
The following loop calculates the sum of the integers 5 + 4 + 3 +2 + 1:

## Slide 71: Your turn . . . (9 of 12)
-128
+127
If the relative offset is encoded in a single signed byte,
  what is the largest possible backward jump?
  what is the largest possible forward jump?

## Slide 72: Your turn . . . (10 of 12)
mov ecx,0
X2:
inc ax
loop X2
4,294,967,296
How many times will the loop execute?
mov ax,6
mov ecx,4
L1:
inc ax
loop L1
10
What will be the final value of AX?

## Slide 73: Nested Loop
.data
count DWORD ?
.code
mov ecx,100 ; set outer loop count
L1:
mov count,ecx ; save outer loop count
mov ecx,20 ; set inner loop count
L2: .
  .
  loop L2 ; repeat the inner loop
mov ecx,count ; restore outer loop count
loop L1 ; repeat the outer loop
If you need to code a loop within a loop, you must save the outer loop counter's ECX value. In the following example, the outer loop executes 100 times, and the inner loop 20 times.

## Slide 74: Summing an Integer Array
.data
intarray WORD 100h,200h,300h,400h
.code
  mov edi,OFFSET intarray ; address of intarray
  mov ecx,LENGTHOF intarray ; loop counter
  mov ax,0 ; zero the accumulator
L1:
  add ax,[edi] ; add an integer
  add edi,TYPE intarray ; point to next integer
loop L1 ; repeat until ECX = 0
The following code calculates the sum of an array of 16-bit integers.

## Slide 75: Your turn . . . (11 of 12)
What changes would you make to the program on the previous slide if you were summing a doubleword array?

## Slide 76: Copying a String
good use of SIZEOF
.data
source BYTE "This is the source string",0
target BYTE SIZEOF source DUP(0)
.code
mov esi,0 ; index register
mov ecx,SIZEOF source ; loop counter
L1:
mov al,source[esi] ; get char from source
mov target[esi],al ; store it in the target
inc esi ; move to next character
loop L1 ; repeat for entire string
The following code copies a string from source to target:

## Slide 77: Your turn . . . (12 of 12)
Rewrite the program shown in the previous slide, using indirect addressing rather than indexed addressing.

## Slide 78: What's Next (5 of 5)
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions
64-Bit Programming

## Slide 79: 64-Bit Programming
MOV instruction in 64-bit mode accepts operands of 8, 16, 32, or 64 bits
When you move a 8, 16, or 32-bit constant to a 64-bit register, the upper bits of the destination are cleared.
When you move a memory operand into a 64-bit register, the results vary:
  32-bit move clears high bits in destination
  8-bit or 16-bit move does not affect high bits in destination

## Slide 80: More 64-Bit Programming
MOVSXD sign extends a 32-bit value into a 64-bit destination register
The OFFSET operator generates a 64-bit address
LOOP uses the 64-bit RCX register as a counter
RSI and RDI are the most common 64-bit index registers for accessing arrays.

## Slide 81: Other 64-Bit Notes
ADD and SUB affect the flags in the same way as in 32-bit mode
You can use scale factors with indexed operands.

## Slide 82: Summary
Data Transfer
  MOV – data transfer from source to destination
  MOVSX, MOVZX, XCHG
Operand types
  direct, direct-offset, indirect, indexed
Arithmetic
  INC, DEC, ADD, SUB, NEG
  Sign, Carry, Zero, Overflow flags
Operators
  OFFSET, PTR, TYPE, LENGTHOF, SIZEOF, TYPEDEF
JMP and LOOP – branching instructions

## Slide 83: 46 69 6E 61 6C

## Slide 84: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.
Notes: If this slide was not included in the original PPT, it should be added.