## Slide 1: Assembly Language for x86 Processors
Copyright © 2020, 2015, 2011 Pearson Education, Inc. All Rights Reserved
Basic Concepts
Chapter 1
Eighth Edition

## Slide 2: Chapter Overview
Welcome to Assembly Language
Virtual Machine Concept
Data Representation
Boolean Operations

## Slide 3: Welcome to Assembly Language
Some Good Questions to Ask
Assembly Language Applications

## Slide 4: Questions to Ask
Why am I learning Assembly Language?
What background should I have?
What is an assembler?
What hardware/software do I need?
What types of programs will I create?
What do I get with this book?
What will I learn?

## Slide 5: Welcome to Assembly Language (cont)
How does assembly language (AL) relate to machine language?
How do C++ and Java relate to AL?
Is AL portable?
Why learn AL?

## Slide 6: Assembly Language Applications
Some representative types of applications:
  Business application for single platform
  Hardware device driver
  Business application for multiple platforms
  Embedded systems & computer games
  (see next panel)

## Slide 7: Comparing ASM to High-Level Languages

## Slide 8: What's Next (1 of 3)
Welcome to Assembly Language
Virtual Machine Concept
Data Representation
Boolean Operations

## Slide 9: Virtual Machine Concept
Virtual Machines
Specific Machine Levels

## Slide 10: Virtual Machines (1 of 2)
Tanenbaum: Virtual machine concept
Programming Language analogy:
  Each computer has a native machine language (language L0) that runs directly on its hardware
  A more human-friendly language is usually constructed above machine language, called Language L1

## Slide 11: Virtual Machines (2 of 2)
Programs written in L1 can run two different ways:
  Interpretation – L0 program interprets and executes L1 instructions one by one
  Translation – L1 program is completely translated into an L0 program, which then runs on the computer hardware

## Slide 12: Translating Languages
Intel Machine Language:
A1 00000000
F7 25 00000004
03 05 00000008
E8 00500000
Assembly Language:
mov eax,A
mul B
add eax,C
call WriteInt
C++: cout << (A * B + C);
English: Display the sum of A times B plus C.

## Slide 13: Specific Machine Levels
(descriptions of individual levels follow . . . )

## Slide 14: High-Level Language
Level 4
Application-oriented languages
  C++, Java, Pascal, Visual Basic . . .
Programs compile into assembly language
(Level 4)

## Slide 15: Assembly Language
Level 3
Instruction mnemonics that have a one-to-one correspondence to machine language
Programs are translated into Instruction Set Architecture Level - machine language (Level 2)

## Slide 16: Instruction Set Architecture (ISA)
Level 2
Also known as conventional machine language
Executed by Level 1 (Digital Logic)

## Slide 17: Digital Logic
next: Data Representation
Level 1
CPU, constructed from digital logic gates
System bus
Memory
Implemented using bipolar transistors

## Slide 18: What's Next (2 of 3)
Welcome to Assembly Language
Virtual Machine Concept
Data Representation
Boolean Operations

## Slide 19: Data Representation
Binary Numbers
  Translating between binary and decimal
Binary Addition
Integer Storage Sizes
Hexadecimal Integers
  Translating between decimal and hexadecimal
  Hexadecimal subtraction
Signed Integers
  Binary subtraction
Character Storage

## Slide 20: Binary Numbers (1 of 2)
Digits are 1 and 0
  1 = true
  0 = false
MSB – most significant bit
LSB – least significant bit
Bit numbering:

## Slide 21: Binary Numbers (2 of 2)
Every binary number is a sum of powers of 2
Each digit (bit) is either 1 or 0
Each bit represents a power of 2:

## Slide 22: Translating Binary to Decimal
Weighted positional notation shows how to calculate the decimal value of each binary bit:
dec = (Dn-1 3 2n-1) + (Dn-2 3 2n-2) + ... + (D1 3 21) + (D0 3 20)
D = binary digit
binary 00001001 = decimal 9:
(1 3 23) + (1 3 20) = 9

## Slide 23: Translating Unsigned Decimal to Binary
37 = 100101
Repeatedly divide the decimal integer by 2. Each remainder is a binary digit in the translated value:

## Slide 24: Binary Addition
Starting with the LSB, add each pair of digits, include the carry if present.

## Slide 25: Integer Storage Sizes
What is the largest unsigned integer that may be stored in 20 bits?
Standard sizes:

## Slide 26: Hexadecimal Integers
Binary values are represented in hexadecimal.

## Slide 27: Translating Binary to Hexadecimal
Each hexadecimal digit corresponds to 4 binary bits.
Example: Translate the binary integer 000101101010011110010100 to hexadecimal:

## Slide 28: Converting Hexadecimal to Decimal
Multiply each digit by its corresponding power of 16:
dec = (D3 3163) + (D23162) + (D13161) +
(D0 3160)
Hex 1234 equals (13163) + (23162) + (33161) + (43160), or decimal 4,660.
Hex 3BA4 equals (33163) + (11 * 162) + (103161) + (43160), or decimal 15,268.

## Slide 29: Powers of 16
Used when calculating hexadecimal values up to 8 digits long:

## Slide 30: Converting Decimal to Hexadecimal
decimal 422 = 1A6 hexadecimal

## Slide 31: Hexadecimal Addition
Important skill: Programmers frequently add and subtract the addresses of variables and instructions.
21 / 16 = 1, rem 5
1
1
36 28 28 6A
42 45 58 4B
78 6D 80 B5
Divide the sum of two digits by the number base (16). The quotient becomes the carry value, and the remainder is the sum digit.

## Slide 32: Hexadecimal Subtraction
Practice: The address of var1 is 00400020. The address of the next variable after var1 is 0040006A. How many bytes are used by var1?
C6 75
A2 47
24 2E
-1
16 + 5 = 21
When a borrow is required from the digit to the left, add 16 (decimal) to the current digit's value:

## Slide 33: Signed Integers
If the highest digit of a hexadecimal integer is > 7, the value is negative. Examples: 8A, C5, A2, 9D
The highest bit indicates the sign.1 = negative, 0 = positive

## Slide 34: Forming the Two's Complement
Note that 00000001 + 11111111 = 00000000
Negative numbers are stored in two's complement notation
Represents the additive Inverse

## Slide 35: Binary Subtraction
Practice: Subtract 0101 from 1001.
0 0 0 0 1 1 0 0 0 0 0 0 1 1 0 0
– 0 0 0 0 0 0 1 1 1 1 1 1 1 1 0 1
0 0 0 0 1 0 0 1
When subtracting A – B, convert B to its two's complement
Add A to (–B)

## Slide 36: Learn How To Do the Following:
Form the two's complement of a hexadecimal integer
Convert signed binary to decimal
Convert signed decimal to binary
Convert signed decimal to hexadecimal
Convert signed hexadecimal to decimal

## Slide 37: Ranges of Signed Integers
Practice: What is the largest positive value that may be stored in 20 bits?
The highest bit is reserved for the sign. This limits the range:

## Slide 38: Character Storage
Character sets
  Standard ASCII (0 – 127)
  Extended ASCII (0 – 255)
  ANSI (0 – 255)
  Unicode(0 – 65,535)
Null-terminated String
  Array of characters followed by a null byte
Using the ASCII table
  back inside cover of book

## Slide 39: Numeric Data Representation
next: Boolean Operations
pure binary
  can be calculated directly
ASCII binary
  string of digits: "01010101"
ASCII decimal
  string of digits: "65"
ASCII hexadecimal
  string of digits: "9C"

## Slide 40: What's Next (3 of 3)
Welcome to Assembly Language
Virtual Machine Concept
Data Representation
Boolean Operations

## Slide 41: Boolean Operations
NOT
AND
OR
Operator Precedence
Truth Tables

## Slide 42: Boolean Algebra
Based on symbolic logic, designed by George Boole
Boolean expressions created from:
  NOT, AND, OR

## Slide 43: NOT
Inverts (reverses) a boolean value
Truth table for Boolean NOT operator:

## Slide 44: AND
Digital gate diagram for AND:
Truth table for Boolean AND operator:

## Slide 45: OR
Digital gate diagram for OR:
Truth table for Boolean OR operator:

## Slide 46: Operator Precedence
Examples showing the order of operations:

## Slide 47: Truth Tables (1 of 3)
Example: X  Y
A Boolean function has one or more Boolean inputs, and returns a single Boolean output.
A truth table shows all the inputs and outputs of a Boolean function

## Slide 48: Truth Tables (2 of 3)
Example: X   Y

## Slide 49: Truth Tables (3 of 3)
Two-input multiplexer
Example: (YS)  (X S)

## Slide 50: Summary
Assembly language helps you learn how software is constructed at the lowest levels
Assembly language has a one-to-one relationship with machine language
Each layer in a computer's architecture is an abstraction of a machine
  layers can be hardware or software
Boolean expressions are essential to the design of computer hardware and software

## Slide 51: Extra
What do these numbers represent?
54 68 65 20 45 6E 64

## Slide 52: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.
shut the fuck up
MIT LICENSE HAHAHAHA
Notes: If this slide was not included in the original PPT, it should be added.